## Slide 1
ECE 362 Embedded Microcontroller Mini-Project  Fall 2016
Team 01 – Cruise Control HUD
Digijock(ette)-Strength Digital System DesignTM
Overview
Cruise control HUD aims to help drivers by dynamically displaying data about the car’s velocity, distance to oncoming cars, and whether to slow down or speed up.
LIDAR
ATD
SPI
SCI
OBD-to-TTL converter
OBD Port
Shift Registers
7 Segment Displays
9S12C
Team Members: Patrick May, Will Pierce, Tyler Carter
PWM
Speed up/ Slow down LEDs
On-Chip Peripherals Detail
This project uses the ATD to receive a PWM signal from the LIDAR, the TIM module to control LED refresh rates and LIDAR sampling, the SCI to communicate with the car, and the SPI module to drive 7-segments through a shift register.
Implementation
This project obtains its speed measurement by continuously polling a speed reading via SCI from the Engine Control Unit (ECU) of a car through the OBD port. Distance measurements are obtained by triggering a distance measurement on the LIDAR and then reading the value the LIDAR responds with using and ATD to calculate how long the pulse is and converting that to a distance. These inputs are then shifted out via SPI to external shift registers which drive 7-segment LEDs.
Power
Car
Circuit Schematic
Board layout
https://youtu.be/xGuQt2sF4p8
Additional Design Work
The PCB was created in Eagle and produced at OSHPark. 3D-printed enclosures for both the LIDAR and boards Autodesk Fusion and printed on a Printrbot Simple Metal. The LIDAR is attached to the hood of a car using neodymium magnets
LIDAR in its enclosure attached to a car
The displays reflecting off the windshield
Project in Operation
“The HUD that will help your BFFAM improve his driving skills”
Additional Circuitry
The main board interfaces to a MAX232 mounted on a perfboard. This is then interfaced to a Sparkfun OBD-to-UART board.
Future Work
Consolidating all circuitry to a single board and using solderless connectors to “foolproof” the design.